## Slide 1
Objective
CW | Resistivity | 26/05/2016
From my learning today I will be able to: | 
Key: | Describe what factors effect Resistance D/C
Boost: | Explain what Superconductivity is and suggest its applications C/B
Aspire: | Apply understanding to graphically workout resistivity B/A
What factors effect resistance?
Explain how?

## Slide 2: Resistivity (ρ)
Experiments show that the resistance of a conductor is:
1. proportional to its length, L
2. inversely proportional to its cross-section area, A
and so: R α L / A

## Slide 3
The constant of proportionality is the
resistivity, ρ of the conductor
Therefore: R = ρ L A
Resistivity is measured in ohm-metre, Ωm.
Resistivity equation demo at Phet
KT resistivity simulation

## Slide 5: Variation in resistivity
Metals and other good conductors have very low resistivities.
(e.g. copper = 1.7 x 10 – 8 Ωm)
Good insulators have very high resistivities.
(e.g. PVC = 1.0 x 10 + 14 Ωm)
Semiconductors have intermediate resistivities.
(e.g. silicon = 2.3 x 10 + 3 Ωm)
Resistivity table on Wikipedia

## Slide 6
Resistivity table on Wikipedia

## Slide 7
1. Calculate the resistance of a 0.30m length of copper wire of cross-section area 5 x 10-6 m2 [resistivity of copper = 1.7 x 10-8 Ωm]
R = ρ L A
= (1.7 x 10-8 Ωm) x (0.30m) / (5 x 10-6 m2)
= 0.00102 Ω = 1.02 mΩ
2. Repeat the above question, this time with silicon [resistivity of silicon = 2300 Ωm]
= (2300 Ωm) x (0.30m) / (5 x 10-6 mm2)
= 1.38 x 108 Ω = 138 MΩ

## Slide 8: 3. Calculate the resistivity of a metal wire of cross-section diameter 0.4mm if a 25cm length of this wire has a resistance of 6Ω.
A = πd2
4
= π x (4 x 10 - 4 m)2 / 4
= π x (1.6 x 10 - 7 m2) / 4
cross-section area = 1.2566 x 10 - 7 m2
ρ = RA
L
= (6 Ω) x (1.2566 x 10 - 7 m2 ) / (0.25 m)
resistivity = 3.02 x 10 - 6 Ωm

## Slide 10
Requirements
constantan wire of diameter 0.27 mm or 0.56 mm, power supply, 0–12 V dc, 2 digital multimeters, micrometer screw gauge, 4 mm leads.
Measuring resistivity
The Graphical method
R =
A
ρ l
x
y

## Slide 11: Superconductivity
Superconductivity is a state where certain materials have zero resistivity.
This occurs at and below a critical temperature (Tc) which depends on the material.
Tc is usually below – 200oC.
Applications include:
  very strong electromagnets (e.g. in MRI scanners)
  power cables to prevent wastage of electrical energy (e.g. to supply the LHC)

## Slide 14
Give the equation for resistivity.
What is superconductivity? When does it occur? Give two applications.
Calculate the resistance of a copper wire of diameter 1mm and length 3m.
Compare the resistivities of copper, silicon and PVC.
Complete the worksheet

## Slide 15: Homework for Next lesson
Read Required Practical 5 notes and prepare:
  Equipment list
  Method
  Risk assessment
  Table of Results
Complete Exam Questions