## Slide 1: AC Generators
Describe the main features of an AC generator
Explain the shape of the voltage waveform
Explain two changes to the voltage waveform if the coil is turned faster

## Slide 2
AC Generator
State the parts of an AC Generator?
Explain how the generators work?
Suggest why the current is AC?

## Slide 3
Task
Explain the shape of the graph you have sketched. What would happen if the coil turned faster?
Extension
Explain these changes in the waveform by referring to Faraday’s law.

## Slide 5: AC Generator
Spinning a coil of wire inside a constant magnetic field means that the angle that the wires cut the magnetic field lines changes over time.
This means that the flux linkage changes over time.
Flux linkage for N coils at angle θ is given as:
The frequency of the spinning magnet can be used to calculate the angle θ:

## Slide 6: AC Generator
Flux linkage for N coils at time t (after angle θ was zero) is given as:
Any formula containing 2πf is often shortened to the following, called the angular frequency:

## Slide 7: Emf
The gradient of a graph of flux linkage against time is the change in flux linkage per second so it is a way of calculating emf
ε0 = Peak p.d.
f = Frequency

## Slide 8: D.C. Generator
Using a split-ring commutator you can create a DC current from a spinning coil of wire
Although the current is always in the same direction, the spinning coil still creates a changing emf over time

## Slide 9: Three phase alternator
A power station uses static coil windings outside of a spinning electromagnet. This creates 3 AC currents that are 120o out of phase to each other.
Transformers and sub-stations can supply these to businesses and homes 1/3 to each.

## Slide 10: Current supplied from a 3 phase coil generator

## Slide 11: Summary
Flux linkage for N coils at time t (after angle θ was zero) is given as:
The gradient of a graph of flux linkage against time is the change in flux linkage per second so it is a way of calculating emf:

## Slide 12
AC current is a sine wave, as is the emf, over time
DC from a spinning coil is a wave but is always positive
UK mains electricity is created in three phases, only one phase is used by any one consumer.