## Slide 1: Magnetic fields 3
Induction

## Slide 2: Objectives
Define Magnetic flux
Describe the process of induction
State Faradays Law & Lenz Law
Calculate the induced EMF

## Slide 3: Recap
Flux density
F=BIL (left hand rule)
  Electric Motors, Moving charges
F= BQv = Bev
  Cyclotrons, mass spectrometers

## Slide 4: Magnetic Flux  (linkage)
The magnetic field strength, B, multiplied by the area swept out by a conductor, A,
 = BA
Unit is the Weber
Flux Linkage for loops of wire = BAN
N= number of loops

## Slide 5: Quick Practice
Copper strip 1cm x 5cm sitting perpendicular to a 0.5T field.
What is the Flux?
A=0.01 x 0.05 = 5x10-4 m2
Flux = B x A = 0.5 x 5x10-4
= 2.5x10-4 Wb

## Slide 6: Induced EMF
Passing a wire through a changing magnetic field and an EMF magically appears.
We call this magic, “INDUCTION”

## Slide 7: Faradays Law
For a wire
EMF = d/dt ( = Flux)
For a coil
EMF = N (d/dt) (N=number of loops)
Induced EMF is equal to the rate of change of flux. (linkage through a circuit)

## Slide 8: EMF = d/dt
What happens if have a higher Flux?
  Irrelevant! It’s the change in flux!
Ok! what If the Flux change is greater?
  Higher EMF
What happens if I change the flux quicker?
  Higher EMF (but obviously for a shorter time)

## Slide 9: Quick Practice
I move my copper strip towards the North Pole of a magnet such that the Flux Changes from 5mWb to 55mWb in 0.5 second.
The Strip has a perfect Voltmeter attached across it. What value does it read?
d = 50x10-3 dt =0.5  EMF = 100x10-3 V

## Slide 10: Lenz’s Law
"the EMF induced in an electric circuit always acts in such a direction that the current it drives around a closed circuit produces a magnetic field which opposes the change in magnetic flux."

## Slide 11: Lenz’s Law
Conservation of Energy!
d/dt  EMF  Current
Current  Field  Force
The induced field is opposite
The force opposes the motion
N S
S N
N S
Notes: Use IWB to draw field lines

## Slide 12: How to change the flux?
Move the conductor
Move the Field
Change the Field

## Slide 13: Moving the conductor
A wire can “sweep out” and area
A = (L)ength X Width (s)wept out
 = BA = BLs
EMF = d/dt = BLs/dt
(s/dt = velocity!)
EMF = BLv
Moving the field would be exactly the same!
L A
s

## Slide 14: Changing the field (loop)
Flux  = BAN
EMF = d/dt
EMF = dB AN/dt

## Slide 15: Nice demo
http://youtube.com/watch?v=fxC-AEC0ROk

## Slide 16: EVEN BETTER DEMO
Why does the ring levitate?
Why doesn’t the split ring levitate?
Why did we use aluminium?

## Slide 17
126 q 1 - 4

## Slide 18: Transformers
An application of physics in disguise

## Slide 19: Objectives
By the end of the lesson you should be able to:
State practical setup of Transformers
Calculate Current and Voltage

## Slide 20: NICE SIMPLE EQUATION 
Primary coil creates a changing flux, which induces a EMF in the secondary coil
N1 V1 = N2 V2
also
Power1= Power2