## Slide 1: Pollution
General properties of Pollution
http://www.youtube.com/watch?v=kdDSRRCKMiI
Objectives
To know the definition of pollution
To describe and explain the properties of pollution

## Slide 2: Specification – 3.4 Pollution

## Slide 3: Specification – 3.4 Pollution

## Slide 4: Specification – 3.4 Pollution

## Slide 5: What is Pollution?
‘Pollution is energy or matter released into the environment with
the potential to cause adverse changes to an ecosystem’
They are usually released by human activities but natural events can produce similar effects.’
‘e.g. heat pollution, air pollution, groundwater pollution.
http://www.youtube.com/watch?v=aA8M9GUMEBA#t=15
Brainstorm: what human activities might cause pollution

## Slide 6: Human activities that cause pollution?
Fuel combustion
Fuel extraction
Manufacturing
Domestic and industrial waste
Pesticides and fertilisers

## Slide 7: Pollution Disasters - Research
Find a pollution disaster that have occurred recently that have caused catastrophic effects on the environment
  5 mins
  Read and summarise the causes and effects of the disaster
    Consider the following:
    Type of pollution
    What caused the pollution in the first place
    Direct and indirect effects of the pollution
    How the pollutant arrived in the environment
    Did the pollution spread and how?
    Clean up operation – was there a method to clean up pollution.

## Slide 8: Behaviour of pollutants
All pollutants have sources, pathways and sinks
The properties of a pollutant determine where it travels and for how long it acts
By understanding how the properties of pollutants have caused problems we can predict the effect of new materials & anticipate/ prevent pollution problems
  SOURCE: where pollution comes from
  PATHWAY: route taken by pollutant
  SINK: where it ends up
CHRONIC EFFECT: Causes effects over long periods of time (weakening organism so that it succumbs to another pollutant or disease);
ACUTE EFFECT: Causes rapid death

## Slide 9: Point sources
Point sources – identifiable source and effect
E.g. power stations, oil refinery, large factories
Easy to see the effects mainly around source, diminishing as distance from source increases. https://earth.nullschool.net/#current/wind/surface/level/orthographic=-69.13,23.51,357

## Slide 10: Diffuse sources
Pollutants released from a large number of small sources.
Difficult to judge effects as spread over large area and difficult to link to single source.

## Slide 11: Direct and Indirect effects
Direct effect
pollutant causes harm by contact with or ingestion by organism
e.g. ionising radiation, acid rain (leaf cuticles), DDT (insects and thin egg shells and sterility in birds)
Indirect effect
pollutant doesn’t harm the organism directly but does so by harming the environment
e.g. acid rain may acidify soils, killing the food plant of a herbivore. Or CO2 and climate change.

## Slide 12: Properties of pollutants
State of matter
Energy form
Density
Persistence
Toxicity
Specificity
Reactivity
Primary & secondary pollutants
Adsorption
Solubility in lipids/water
Bioaccumulation
Biomagnification
Synergism
Mutagentic action
Teratogenic action
Mobility
The properties of pollutants determine the length of time it may cause a problem, the level of harm and where and how far

## Slide 13: Activity
Groups 4
Select a property of pollutants
Research the property (Text book Pgs 236-240)
Make a flash card for that property
  Include definition
  Examples

## Slide 14: State of matter
State of matter will affect the pollutants ability to be dispersed by water or air.
Solids tend to be deposited close to the source.
Gases easily dispersed in the atmosphere

## Slide 15: Energy form
Different pollutants have different energy forms (noise, heat, ioninsing radiation, light) and this will affect how they behave in the environment.

## Slide 16: Density
Density affects dispersal.
More dense pollutants require more kinetic energy to keep them suspended (either in air/water) so are deposited close to the source.
E.g. hydrogen cyanide (Bhopal disaster 1984) is denser than air so settled close to the ground.

## Slide 17: Persistence
Measure of how long it takes for a pollutant to chemically break down.
Persistence can be measured as the time it takes for half of the pollutant to break down = environmental half-life. (T ½ ENV)
CFCs, organochlorine insecticides (DDT) – chemically stable and break down slowly = high persistence
Sewage, pyrethroid insecticides = low persistence
Heavy metals are elements so do not break down.

## Slide 18: Toxicity
Measure of how poisonous a substrate is, usually caused by enzyme inhibition. Toxins usually damage protein function.
Pollutant | Toxic action
Carbon monoxide | prevents Haemoglobin carrying oxygen in red blood cells
Lead | Inhibits enzymes in nerve cells
Acids | Inhibit protein action by changing the shape of the protein e.g. active sites of enzymes
Cyanide | Inhibits enzymes in aerobic respiration

## Slide 19: Toxicity - examples
DDT
  Dichlorodiphenyltrichloroethane (DDT) is a organochlorine contact insecticide that kills by acting as a nerve poison.
  http://npic.orst.edu/factsheets/ddtgen.pdf
Acids (acid rain or leaching from mine spoil heaps)
  Change the shape of cell membranes and function of proteins so cell membrane does not function properly.
  http://www.youtube.com/watch?v=yGhyJSGnW9g

## Slide 20: Specificity
Measure of the differing toxicities of a substance on different organisms.
A pollutant may be toxic to one organism and much less toxic to others.
E.g. Pyrethoid insecticides
  Low in toxicity to mammals and birds;
  High in toxicity to fish if applied directly to water;
  Require very low doses to kill insects (high arthropod toxicity);
  Fast-acting;
  Especially effective against chewing insects, though many pyrethroid insecticides can be absorbed by the insect pest when it merely walks over the dry residue;
  Bind tightly to soil and organic matter (therefore not as effective in penetrating soil to kill underground pests);
  Dissolve very poorly in water.

## Slide 21: Reactivity
Reactivity affects the severity of the pollution – can increase or reduce the problems caused.
Reactive pollutants may degrade rapidly (e.g. sewage) or react with other substances to produce secondary pollutants
Pollutant | Reactivity | Effect on pollution
CFCs | Low (except in UV) | Stable in the troposphere but broken down in stratosphere releasing chlorine
NOx, ozone, hydrocarbons | High | React with each other to produce PANs which are more toxic

## Slide 22: Primary and Secondary Pollutants
Primary pollutants are released by humans e.g.
CO2 by burning fossil fuels
Oil released in tanker accidents
Pesticides used in agriculture release pollutants
Secondary pollutants are produced by the interaction of other materials release by human activities e.g.
Tropospheric ozone is produced by the interaction of oxides of nitrogen from fuel combustion with O2 in the atmosphere
PANs which cause photochemical smogs, are produced by the interaction of oxides of nitrogen, ozone and unburnt hydrocarbons

## Slide 23: Adsorption
Pollutants that attach to the surface of materials e.g. soil particle or aquatic sediments. This mobilizes them so they can’t cause pollution problems but they may be released later to cause problems e.g. sediments disturbed in a lake by a storm releasing phosphates or PCBs

## Slide 24: Solubility
Water soluble pollutants are often more mobile in the hydrosphere E.g. Nitrates, phosphates
Liposoluble – organic compounds that dissolve in fats and oils can pass through cell membranes and be stored
e.g. mercury, DDT

## Slide 25: Bioaccumulation
The absorption and storage of pollutants in the tissues of organisms increasing the amount in the organism over time
Small doses of pollutants build up to toxic levels
Liposoluble pollutants tend to build up in the body whereas water soluble pollutants can be excreted more easily.

## Slide 26: Biomagnification
http://www.youtube.com/watch?v=xI2M97Gl5qM
http://www.youtube.com/watch?v=E5P-UoKLxlA
Substances become more concentrated as they pass along a food chain. Organisms in higher trophic levels have longer lifespans and build up higher concentrations.

## Slide 27: Difference between Bioaccumulation & Biomagnification

## Slide 28: Synergism
Interaction of 2 or more pollutants to create a greater impact than the sum of their individual impacts
Nitrates and Phosphates cause worse eutrophication together than individually;
A mixture of SO2 & NO2 (from coal burning) may be greater in causing acid rain problems than individually

## Slide 29: Mutagens
A material that can cause changes in DNA = mutation
Gonadic effects (cells in ovaries or testes)
  May causes birth abnormalities
Somatic effects (general body cells)
  May cause uncontrolled cell division = cancer
E.g. Ionising radiation, UV light, Cadmium, asbestos, dioxins and PCBs.

## Slide 30: Carcinogens
A mutagen that causes cancer
Eg asbestos, DDT, cadmium

## Slide 31: Teratogenicity
Non–inherited birth defects (not passed on to future generations)
The interruption of DNA function so that the genes of an unborn embryo cannot cause normal growth and development.
Birth abnormalities may be produced (which are not inherited by future generations).
E.g. Dioxins such as Agent Orange
  http://www.who.int/en/news-room/fact-sheets/detail/dioxins-and-their-effects-on-human-health
Mercury

## Slide 32: Minimata disease http://en.wikipedia.org/wiki/Minamata_disease

## Slide 33: Mobility
Measure of the degree to which the pollutant is carried by wind, water or organisms. Depends on other properties (state of matter, density & solubility in water)
Examples:
  CFCs not soluble so can travel long distances in atmosphere
  Sulfur dioxide dissolves in rain so washed out of atmosphere
  Smoke particles washed out of atmosphere and also settle due to gravity
  Lead dust – high density of atmospheric dust causes most particles to be deposited close to the source

## Slide 34: Effects of environmental features
The environment that a pollutant is released in can have a big impact on the extent and severity of the pollution.
  Features affect degradation
  Factors that affect dispersal

## Slide 35: Degradation
The process of breakdown = degradation
  Biodegradation – caused by living things, usually bacteria
  Photodegradation – caused by light
  Thermal degradation – caused by heat

## Slide 36: Features affecting degradation
Temperature – higher temperatures increase rates of reaction
Light levels – provide activation energy that drive chemical reactions
Oxygen – involve in many reactions e.g.
  aerobic bacterial decomposition of sewage
  oxidation of sulphide ores producing sulfur dioxide
  Oxidation state affects the solubility of many metals
pH – affects the solubility of substances e.g. heavy metals are more soluble in acid conditions
Pollutant interactions – one pollutant may be affected by another e.g.
  Nox and hydrocarbons in photochemical smogs
  Combined effect of phosphates and nitrates in eutrophication

## Slide 37: Factors affecting dispersal
Wind & water currents:
  Affects how far a pollutant is dispersed
Temperature inversions
Presence of adsorbent materials
MWB – Draw a graph to show how the temperature changes with altitude in the troposphere

## Slide 38: Temperature inversions
http://www.youtube.com/watch?v=LPvn9qhVFbM
Demo
Normally temperature goes down with increase altitude in the troposphere. Warm gases at ground level are less dense and rise and disperse.

## Slide 39: Temperature inversions
http://www.youtube.com/watch?v=LPvn9qhVFbM
Demo
Air near the ground is cooler than air above
Pollutant gases less buoyant (denser) and will not rise and disperse so become concentrated. Air near the ground is cooler than air above
Pollutant gases less buoyant (denser) and will not rise and disperse so become concentrated.

## Slide 40: Under normal conditions

## Slide 41: Thermal (temperature) inversion

## Slide 42: Ideal conditions for a temperature inversion
Valleys: the sheltering effect of valleys means that cool, dense air may sink under warmer air without winds dispersing it.
Clear night skies: loss of heat from IR radiation is increased, so the air above the ground cools.
Mist or fog: these reflect sunlight and prevent the ground from warming up as quickly.
Low wind speeds: reduces the mixing of layers of air, which would disperse cooler air below the inversion layer.

## Slide 43: Temperature inversions
Lapse rate diagrams show the relationship between temperature and altitude.

## Slide 44: Presence of adsorbant materials
Materials like clay particles or organic materials in aquatic sediments cause pollutants to adsorb onto them. This immobilises them and stop it causing problems.
Many naturally toxic metal ions are immobilised by being adsorbed onto soil particles e.g. aluminium and lead.

## Slide 45: General Pollution Control
Objectives
To be able to distinguish between critical pathway analysis and critical group monitoring
To understand the main emission control strategies
To describe the principles behind pollution control

## Slide 46: Environmental monitoring
Environment needs to be checked in the places where it is considered that a pollutant may pose a threat to humans. Sampling will be done to monitor levels of pollutant.
Sampling sites tend to be:
  Where wind and water most likely to carry pollutants
  Where people might be harmed
  Where human activities occur (farming, fisheries)
  Monitoring should confirm the accuracy of a CPA (critical pathway analysis)

## Slide 47: Critical pathway analysis
Used to predict the movement of pollutants and to plan monitoring programmes. It can’t be assumed that any discharge will be diluted and dispersed. In the atmosphere and water it can become re-concentrated. (Think & link – water cycle)
Mainly used for movement of radioactive materials released from a nuclear power station or waste processing site. Ensures that sites at most risk are sampled
Factors to take into account:
  State of pollutant (s,l,g)
  Density
  Solubility in water/lipids
  Chemical stability
  Wind speed and direction
  Geology – porosity/permeability
  Effect of pH and O2 on solubility
  Temperature
Properties of the pollutant
Features of the environment

## Slide 48: Critical Group Monitoring
A specific method of assessing the risk of public exposure to pollutants. It will look at members of the public whose lifestyle/job mean they are at risk. If their risk is low then it’s assumed that all other members of the public have an even lower risk.
http://www.youtube.com/watch?v=KxBe6ubGiow

## Slide 49: Emission control strategies
Control of emission location
  Some choices may affect the severity of the pollution caused:
    Marine discharges where water currents will dilute and disperse emissions.
    Emissions downwind of urban areas
    Not discharging waste onto permeable rock above an aquifer
Control of emission timing
  Tidal cycle
    emissions into incoming tide will carry upstream. Emission into outgoing tide will disperse them
  Temperature inversions
    Atmospheric emissions in a temperature inversion will not disperse. Restrict emissions in cities where temperature inversions are common

## Slide 50: Principles of pollution control
The polluter pays principle
  Whoever causes the pollution is responsible for the problems caused and has an obligation to prevent it.
  Costs of preventing are less than costs of damage
  Complying with this is made greater by high financial penalities
The precautionary principle
  It is assumed that a waste will cause pollution until research confirms it’s unlikely to when release is permitted.
  This means being unaware of a problem is not an excuse and does not reduce responsibility

## Slide 51: Selection of Control
Control method | Example
Production prevention | Desulfuristion of fossil fuels
Prevention of release | Electrostatic precipitators for smoke control Catalytic converters for NOx, CO and hydrocarbons
Post-release prevention | Oil spill clean-up methods Phytoremediation of land contaminated with heavy metals
Alternative processes | Use of electric vehicles instead of diesel or petrol Using pyrethroid pesticides instead of more polluting organochlorides (e.g. DDT) Using renewable energy sources

## Slide 52: Efficiency of Pollution Control
Rarely practical to reduce pollution emissions to zero.
Costs of removing pollutants rises sharply as more pollutants are removed, until clean up costs exceed the harmful costs of the pollution
Break-even point = when costs of pollution are the same as clean up costs.
The point is determined by separately plotting clean-up costs and the cost of the pollution to society. The 2 curves are then added together to reveal the total costs
Economic impact of pollution worksheet
http://www.youtube.com/watch?v=KxBe6ubGiow