## Slide 1: Induction
K – describe what happens to the moving conductor in the B-field
B – apply Fleming’s right hand rule
A – explain how a current is induced to flow in the wire

## Slide 2: Generating electricity
What three things do you need to generate electricity?
Movement

## Slide 3
When a moving charge moves it produces a magnetic field.
Similarly when a conductor moves in a magnetic field it causes a current to flow in the conductor. This is called induction. This can also happen if you have a conductor with a magnetic field moving across it.
The condition for induction is that the conductor must cut across the lines of flux.

## Slide 4
Electromagnetic Induction means that an emf (electromagnetic flux) is created when a wire is passed through a magnetic field. If the wire is part of a complete circuit then the emf will create a current flow in the wire.
How can the emf be increased?
Note: No emf is created if the wire is parallel to the magnetic field lines as no magnetic lines will be broken as it moves.
Electromagnetic Induction
Move the wire faster
Use a coil of wire
Use a stronger magnet

## Slide 5
Using a motor in reverse
If a motor is forced to move and it is connected in a circuit then a current will be produced in the circuit.

## Slide 6
Using a dynamo
A dynamo contains a magnet that spins within a coil of wire. This induces an emf in the coil which in turn can produce a current.

## Slide 7: Michael Faraday
1791 - 1867
Credited with discovering electromagnetic induction, his famous quote when asked what electricity is for, he replied:
“What use is a new baby”
and
“Why sir, there is the probability that you will soon be able to tax it”

## Slide 8
The direction of the current can be determined using Fleming’s right hand rule.

## Slide 9
Task
Explain what happens to this conductor as it is moved across this magnetic field.

## Slide 10
Answers
current moves upwards
Conductor cuts across lines of flux
Potential difference induced at the ends of the conductor
Current flows
Electrons move down

## Slide 11: Summary
If a wire is moved in a magnetic field then an emf is created in the wire
If connected to a circuit this emf created a current that carries energy to the components
In a motor the coil moves inside fixed magnets; in a dynamo the magnet moves inside a fixed coil
The following will increase the current:
  Coiling the wire
  Moving the wire faster
  Using a stronger magnet
Flemming’s right-hand rule is used to work out current flow direction