## Slide 1
Forces on a current carrying wire
Wednesday, 06 March 2019
What do you already know about magnets and magnetic fields?

## Slide 2
K – state the factors affecting the force on a current carrying wire in a magnetic field
B – calculate the size of the force on the wire
A – explain the difference in force when the fields are parallel and perpendicular to each other

## Slide 3
    Definition : A magnetic field is a force field which surrounds either a magnet or a wire carrying an electric current and will act upon, without contact, another magnet or current carrying wire

## Slide 4
A current moving inside a wire creates a magnetic field around the wire
The field lines move in a circle around the wire
If the wire is inside another magnetic field the two may exert a force on each other

## Slide 5
When will you get maximum force or no force at all?
If the wire and the magnetic field are at right angles to each other then the force is a maximum
If the wire and the field lines are in the same direction then the force is zero

## Slide 6
    Wires carrying an electric current produce a magnetic field.
    The “right-hand rule” can be used to establish the direction of this field. Note the current direction is the direction of “conventional current” positive to negative

## Slide 7
The three factors that affect the magnitude of the force are:
The magnetic flux density – B
The current in the wire – I
The length of the wire inside the field – l
This gives is the formula F = BIl when the field and wire are at right angles

## Slide 8
We can use Fleming’s left-hand rule to determine the direction the wire will move

## Slide 9: Formula and units
If the current flow is at right angles to the magnetic field then then the following formula can be used:

## Slide 11: Magnetic Flux Density
    For a given magnetic field, the Force on a current-carrying wire (when perpendicular to the field) is equal to:
    Where is the current, is the length of the wire, and B is the Magnetic flux density, equal to the force per unit length per unit current.
    Unit of Magnetic flux: NA-1m-1 but given the unit of Tesla (T) (therefore 1T = 1 NA-1m-1)

## Slide 12
    A straight horizontal wire of length 5m is in a uniform magnetic field which has a magnetic flux density of 120mT. The wire is perpendicular to the field lines which act due North. When the wire conducts a current of 14A from East to West calculate the magnitude and direction of the force on the wire.
    F = 120 x 10-3 x 14 x 5
    F = 8.4N
    Vertically downwards
Current East to West
Field due North

## Slide 13: Answers
Force | Magnetic flux density | Current | Length
20 N | 0.3 T | 7 A | 9.52 m
3 N | 1 mT | 20 A | 150 m
500 N | 33 T | 200 mA | 75.8 m
67 N | 0.4 T | 2.5 A | 67 m
6 kN | 4 T | 60 A | 25 m
Complete:

## Slide 14: Problems
2.4 x 10-2N West
4.5A East to West
0.2T Vertically down
South
8.0 x 10-3N

## Slide 15
The Motor Effect
06/03/2019
K – describe the construction of a DC motor
B – state the factors which increase the speed of the motor
A – explain how the DC motor works

## Slide 16
Name 5 things that have an electric motor in.
In each device what does the motor do?

## Slide 17
    Looking from above :
F
F
w
Coil Parallel to field. Torque =
F
F

Coil now at an angle  to the field. Torque =
    But
    is the area of the coil giving
    When the coil is parallel to field ( =0, cos 0 = 1), the torque is BIAn. When the coil is perpendicular ( =90, cos 90 = 0), the torque is zero.
X
Y
X
Y

## Slide 20
The current flows in different directions on each side of the coil
This means the force on each side is in the opposite direction
This creates a couple which turns the coil
Every half-turn the current flows again and there is another force to keep the coil turning

## Slide 21
Write an explanation of how the DC Motor works. Include as much detail as you can.

## Slide 22
Current flows around the coil when the brushes connect
This current produces a magnetic field around the wire
On opposite sides of the coil the current is in opposite directions
This means the force acting on each side is in opposite directions producing a couple
The couple produces a turning effect on the coil
Every half turn the current reconnects and a force acts to continue turning the coil
The motor can be speeded up by (name 2 of) increasing the current, adding more coils, increasing the magnetic field strength of the magnet or moving the magnet closer to the coils
1-2 = D, 3-4=C, 5=B, 6=A