## Slide 1
Current and charge quiz
1. Calculate the charge passing through a lamp in three minutes when a steady current of 0.4 A is flowing.
Q = I t
Q = 0.4 x 3 x 60 = 72 Coulomb
I =
Q
t

## Slide 2
Current and charge quiz
2. Calculate the number of electrons flowing through a resistor when a current of 2.3 flows for 5 minutes
Q = I x t
Q = 2.3 x 5 x 60 = 690 Coulomb
no. of electrons = 690 /1.6x10-19 = 4.31x1021
I =
Q
t

## Slide 3
Current and charge quiz
3. What is the current in a circuit if 2.5x1020 electrons pass a given point every 8 seconds
Charge (C) =
no. of electrons x charge of one electrons
Charge (C) =
2.5x1020 x 1.6x10-19 = 40 Coulombs
I =
Q
t
Current = 40/8 = 5 Amps

## Slide 4
Current and charge quiz
4. How long does it take for a current of 0.3A to supply a charge of 48C?
t = Q/I
t = 48/0.3 = 160 seconds
I =
Q
t

## Slide 5
Current and charge quiz
5. How many electrons pass a point when a current of 0.4A flows for 900 seconds?
Q = I x t = 0.4 x 900 = 360 Coulomb
I =
Q
t
no. of electrons = total charge / charge of one electron
no. of electrons = 360 / 1.6 x 10-19 = 2.25 x 1021

## Slide 6
Current and charge quiz
6. A torch bulb passes a current of 120 mA.
How many coulombs of charge flow through the lamp in 1 minute?
Q = I x t = 120x10-3 x 60 = 7.2 Coulomb

## Slide 7
Current and charge quiz
7. A car battery is rated as 36 A h.
In principle this means it could pass a current of 1 A for 36 h before it runs down. How much charge passes through the battery if it is completely run down?
Q = I x t = 1 x 36 x 60 x 60 = 129600 Coulomb

## Slide 8
Current and charge quiz
8. An electron beam in a beam tube carries a current of 125 A.
(a) What charge is delivered to the screen of the tube every second?
(b) How many electrons hit the screen each second?
Q = I x t = 125 x 10-6 x 1 = 125 x 10-6 Coulomb
no. of electrons = 125 x 10-6 / 1.6x10-19 = 7.8 x 1014
(a)
(b)