## Slide 1
AQA
    AS Level
      Computer Science
      Paper 2
Logic gates
  Unit 4
  Hardware and software

## Slide 2
Construct truth tables for a variety of logic gates
Be familiar with drawing and interpreting logic gate circuit diagrams involving multiple gates
Complete a truth table for a given logic gate circuit
Write a Boolean expression for a given logic gate circuit
Draw an equivalent logic gate circuit for a given Boolean expression
Objectives

## Slide 3
Binary switches
Electronic devices can only recognise the presence or absence of a current
Computers comprise billions of switches which can either be ON or OFF
These switches can be combined in different ways to create simple circuits called logic gates
Output
A
B
Input
Output
A
B
Input

## Slide 4
Logic gates
Electronic logic gates take one or more inputs and produce a single output
The output can then become the input to the next gate, and so on, to create a complex circuit
  A number of logic gates are designed to produce different outputs for the various possible combinations of ON or OFF inputs

## Slide 5
Logic gates
The six gates studied in this unit are:
NOT, AND, OR, XOR, NAND, NOR
Each of these can be represented by a graphical symbol and a truth table showing the output for each possible input or combination of inputs

## Slide 6
NOT gate
If 0 is input it outputs 1
If 1 is input it outputs 0
Logic Diagram
Truth Table
INPUT
A
OUTPUT
P
Boolean algebra: P = NOT A
In Boolean notation:
A | P
0 | 1
1 | 0

## Slide 7
AND gate
If both inputs are 1 then the output is 1
Otherwise the output is 0
Logic Diagram
Truth Table
INPUT
A
Boolean algebra: P = A AND B
In Boolean notation:
INPUT
B
OUTPUT
P
A | B | P
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 8
OR gate
If either input is 1 then the output is 1
Otherwise the output is 0
Logic Diagram
Truth Table
INPUT
A
Boolean algebra: P = A OR B
In Boolean notation:
INPUT
B
OUTPUT
P
A | B | P
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 9
Creating logic circuits
Multiple logic gates can be connected to produce an output based on multiple inputs
INPUT
A
OUTPUT
R
OUTPUT
P
INPUT
B
Boolean algebra:
P = NOT (A AND B)
In Boolean notation:
A | B | R = A AND B | P = NOT R
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 10
Creating logic circuits
Multiple logic gates can be connected to produce an output based on multiple inputs
INPUT
A
OUTPUT
R
OUTPUT
P
INPUT
B
Boolean algebra:
P = NOT (A AND B)
In Boolean notation:
A | B | R = A AND B | P = NOT R
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 11
Increasing the number of inputs
With three inputs, how many possible combinations of 0 and 1 are there?
OUTPUT
P
INPUT
A
INPUT
B
INPUT
C
R
Boolean algebra:
P = (A AND B) OR C
In Boolean notation:
P = (A • B) + C

## Slide 12
Combining logic gates
OUTPUT P
INPUT A
INPUT B
INPUT C
R
A | B | C | R = A AND B | P = R OR C
0 | 0 | 0 |  | 
0 |  |  |  | 
0 |  |  |  | 
0 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
1 |  |  |  | 
Boolean algebra:
P = (A AND B) OR C
In Boolean notation:
P = (A • B) + C

## Slide 13
Combining logic gates
OUTPUT P
INPUT A
INPUT B
INPUT C
R
A | B | C | R = A AND B | P = R OR C
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
Boolean algebra:
P = (A AND B) OR C
In Boolean notation:
P = (A • B) + C

## Slide 14
Worksheet 5
Now try the questions in Task 1

## Slide 15
XOR (Exclusive OR) gate
If one, but not both, of the inputs is 1, the output is 1
Otherwise the output is 0
A | B | P
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
INPUT
A
INPUT
B
OUTPUT
P
Boolean algebra: P = A XOR B
Boolean notation: P = A ⊕ B
Logic Diagram
Truth Table

## Slide 16
NAND gate
This is an amalgamation or the AND and NOT gate
It inverts the output of the AND gate
A | B | P
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
INPUT
A
INPUT
B
OUTPUT
P
Boolean algebra: P = NOT (A AND B)
Boolean notation: P =
Logic Diagram
Truth Table

## Slide 17
NOR (NOT OR) gate
This gate inverts the OR gate
The output is 1 only if both inputs are 0
INPUT
A
INPUT
B
OUTPUT
P
Boolean algebra: P = NOT (A AOR B)
Boolean notation: P =
A | B | P
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Logic Diagram
Truth Table

## Slide 18
NAND – The universal gate
The NAND gate is useful as it combines the functions of two gates in a single gate
The NAND gate is known as a universal gate because different combinations of NAND gates can act like NOT, OR and AND gates
In fact, any circuit can be built using just NAND gates

## Slide 19
NAND or NOT?
Are the following two gates equivalent?

## Slide 20
Advantages of NAND gates
Using only NAND gates to build a circuit can minimise cost of production
Using as few gates as possible can speed up processing

## Slide 21
Worksheet 5
Now try the questions in Task 2

## Slide 22
Plenary
There are six logic gates that you need to be familiar with
Be sure you can :
  Write truth tables for each of them
  Write a Boolean expression for a given logic gate circuit
  Draw an equivalent logic gate circuit for a given Boolean expression