## Slide 1
Objective
CW | More about Resistance - Resistor Combination | 07/06/2016
From my learning today I will be able to: | 
Key: | State the rules for resistance in Series and parallel D/C
Boost: | Derive the rules and use them to calculate values in a circuit C/B
Aspire: | Apply knowledge to complex circuit applications B/A
Which bulbs are brighter - why?
What can we say about the Currents in each?
How does this connect to resistance?

## Slide 2: Resistors in series
Resistors in series pass the same current, I.
The total potential difference across the two resistors, V is equal to the sum of the individual pds:
V = V1 + V2
Netfirms resistor combination demo
Multimedia combination calculator

## Slide 3
The pd across R1, V1 is given by: V1 = I R1
and across R2, V2 = I R2
The total pd,V across the total resistance RT is equal to I RT
but: V = V1 + V2
= I R1 + I R2
therefore: I RT = I R1 + I R2
as all the currents (I) cancel
so: RT = R1 + R2
RT = R1 + R2 + R3 + …
The total resistance is always greater than any of the individual resistances
Netfirms resistor combination demo Multimedia combination calculator

## Slide 4: Resistors in parallel
Resistors in parallel all have the same pd, V.
The total current through the two resistors, I is equal to the sum of the individual currents:
I = I1 + I2
Netfirms resistor combination demo Multimedia combination calculator

## Slide 5
The current through R1, I1 is given by: I1 = V / R1
and through R2, I2 = V / R2
The total current, I through the total resistance, RT is equal to V / RT
but: I = I1 + I2
= V / R1 + V / R2
therefore: V / RT = V / R1 + V / R2
as all the p.d.s (V) cancel
so: 1 / RT = 1 / R1 + 1 / R2
1 = 1 + 1 + 1 …
RT R1 R2 R3
The total resistance is always smaller than any of the individual resistances
Netfirms resistor combination demo Multimedia combination calculator

## Slide 6
(a) series
RT = R1 + R2
= 4 Ω + 6 Ω
= 10 Ω
(b) parallel
1 / RT = 1 / R1 + 1 / R2
= 1 / (4 Ω) + 1 / (6 Ω)
= 0.2500 + 0.1666
= 0.4166
= 1 / RT !!!!
and so RT = 1 / 0.4166
= 2.4 Ω
Calculate the total resistance of a 4 and 6 ohm resistor connected (a) in series, (b) in parallel.

## Slide 7
 | Voltage | Current | Resistance
Series |  |  | 
Parallel |  |  | 
Summary
Complete the table to show how each quantity is shared in a circuit

## Slide 8: Calculate the total resistance of the two circuits shown below:
Calculate the parallel section first
1 / R1+2 = 1 / R1 + 1 / R2
= 1 / (2 Ω) + 1 / (5 Ω)
= 0.5000 + 0.2000
= 0.7000
R1+2 = 1.429 Ω
Add in series resistance
RT = 5.429 Ω
= 5.43 Ω (to 3sf)
4 Ω
2 Ω
5 Ω
1.
12 Ω
8 Ω
5 Ω
2.
Calculate the series section first
5 Ω + 8 Ω = 13 Ω
Calculate 13 Ω in parallel with 12 Ω
1 / RT = 1 / R1 + 1 / R2
= 1 / (13 Ω) + 1 / (12 Ω)
= 0.07692 + 0.08333
= 0.16025
RT = 6.2402 Ω
= 6.24 Ω (to 3sf)

## Slide 9
The ammeter below reads 1.0 A. All the resistors have the same value. What is the current through the black resistor?
A
2A

## Slide 10
A5
A7
A1
A8
A6
A4
A3
A2
Ammeter A5 reads 3 A. All the resistors have the same value of 10 Ω. What are the readings on ammeters A1 to A8 ?
A1 = 11 A, A2=6 A, A3=2 A, A4=2 A, A5=3 A, A6=5 A, A7=11 A, A8=11 A

## Slide 11
Calculate the potential difference supplied by the cell in this circuit.
Calculate the current in this circuit.
Calculate the missing resistance in this circuit.

## Slide 12: Undergraduate level question
60 Ω
60 Ω
60 Ω
Calculate the total resistance of the circuit below:
The three resistors are in parallel to each other.
ANSWER: RT = 20 Ω
Hint: Are the resistors in series or parallel with each other?
What are the proofs for the total resistance of resistors connected (a) in series and (b) in parallel.
Calculate the total resistance of a 3Ω and a 7Ω resistor connected (a) in series and (b) in parallel.
Complete the worksheet

## Slide 13
Find the current drawn from the power source.
Circuit current = 2.5 A
5 Ω
Circuit current = 2 A

## Slide 14
Find the potential difference across the 12 Ω resistor.
PD = 3.2 V
I 12 Ω = 4 V / (12 Ω + 3 Ω) = 0.27 A;
V12 Ω = 0.27 A x 12 Ω = 3.2 V

## Slide 15
40Ω
132 Ω
25 Ω
67 Ω
40Ω
50Ω
50Ω
100Ω
200Ω
What is RT ?

## Slide 16
50 Ω
132 Ω
25 Ω
63 Ω
10Ω
20Ω
40Ω
15Ω
25Ω
What is RT ?

## Slide 17
450 Ω
532 Ω
500 Ω
600 Ω
100Ω
200Ω
100Ω
100Ω
100Ω
What is RT ?

## Slide 18
110 Ω
50 Ω
45 Ω
55 Ω
40Ω
50Ω
70Ω
30Ω
What is RT ?

## Slide 19
50 Ω
20 Ω
5 Ω
1 Ω
20Ω
10Ω
10Ω
10Ω
What is RT ?

## Slide 20: Homework for Next lesson
Read through Page 217 and 219 make notes
  Explain how Resistance can be used in real world applications
Complete Work sheet