## Slide 1
1. A typical hand-held torch runs off two 1.5 V cells, yet has a lamp rated at 2.5 V, 0.5 A. Explain how the potential difference across the lamp can actually be 2.5 V as rated. What is the internal resistance of each cell, supposing them to be identical?
1.5V
2.5 V
1.5V
0.5A

## Slide 2
2. A typical car battery has an emf of 12 V, and must provide a current of 80 A to the starter motor. Why must the car battery have a very low internal resistance? If the internal resistance is 0.05 Ω, find the potential difference across this internal resistance when the starter motor is running. Why is starting the car with the headlights on likely to affect their brightness?

## Slide 3
3. Some school laboratories have EHT (Extra High Tension) power packs giving up to 3000 V. For safety, they are provided with a 50 MΩ resistor in series with the supply. What is the maximum current able to be drawn from the supply? Approximately what potential difference would there be across a torch bulb of 10 Ω resistance connected across such a supply?
3000V
10Ω
50MΩ

## Slide 4
4. A student experimenting with a solar cell connects a 1000Ω voltmeter across it and observes a potential difference of 1.0 V. Using a different, extremely high resistance digital voltmeter, the reading is larger, 1.2 V. Why the difference? What is the internal resistance of the solar cell?
V
1000Ω
Infinite resistance
V

## Slide 5
5. A 9.0 V battery has an internal resistance of 12.0 .
(a) What is the potential difference across its terminals when it is supplying a current of 50.0 mA?
(b) What is the maximum current this battery could supply?
(c)Draw a sketch graph to show how the terminal potential difference varies with the current supplied if the internal resistance remains constant. How could the internal resistance be obtained from the graph?

## Slide 6
6. A cell in a hearing aid supplies a current of 25.0 mA through a resistance of 400 . When the wearer turns up the volume, the resistance is changed to 100  and the current rises to 60 mA. What is the emf and internal resistance of the cell?

## Slide 7
7. A battery is connected in series with a variable resistor and an ammeter. When the resistance of the resistor is 10  the current is 2.0 A. When the resistance is 5  the current is 3.8 A. Find the emf and the internal resistance of the battery.

## Slide 8
9. When a cell is connected directly across a high resistance voltmeter the reading is 1.50 V. When the cell is shorted through a low resistance ammeter the current is 2.5 A. What is the emf and internal resistance of the cell?

## Slide 9
Answers

## Slide 10
1. A typical hand-held torch runs off two 1.5 V cells, yet has a lamp rated at 2.5 V, 0.5 A. Explain how the potential difference across the lamp can actually be 2.5 V as rated. What is the internal resistance of each cell, supposing them to be identical?
Emf = 3V
V = 2.5 V
I = 0.5 A
Emf = V + Ir
3 = 2.5 + (0.5 x r)
r = 0.5/0.5 = 1Ω ( for the two cells)
r = 0.5 Ω each
Lost volts = 0.5 V
1.5V
2.5 V
1.5V
0.5A

## Slide 11
2. A typical car battery has an emf of 12 V, and must provide a current of 80 A to the starter motor. Why must the car battery have a very low internal resistance? If the internal resistance is 0.05 Ω, find the potential difference across this internal resistance when the starter motor is running. Why is starting the car with the headlights on likely to affect their brightness?
The car battery has to have a very little internal resistance so it can provide a high current to the starter motor.
r = 0.05Ω
Potential difference across r = Ir = 80x 0.05 = 4V (= lost volts)
The headlights are at normal brightness if the supplied voltage is 12 V
Starting the car with the lights on means that the lights only get 8 V (since 4V is being lost) so they are dim.

## Slide 12
3. Some school laboratories have EHT (Extra High Tension) power packs giving up to 3000 V. For safety, they are provided with a 50 MΩ resistor in series with the supply. What is the maximum current able to be drawn from the supply? Approximately what potential difference would there be across a torch bulb of 10 Ω resistance connected across such a supply?
Emf = 3000V
r= 50 MΩ = 50x106 Ω
Emf = IR+ Ir
Emf = I (R + r)
I = Emf/(R+r)
maximum current is when R = 0 I = 3000/ 50x106 = 6x10-5 A
When R = 10 Ω
I = 3000/ (50x106 +10)= 5.999x10-5 A
Voltage across the bulb = IR = 5.999x10-5 x 10 = 5.999x10-4 V
3000V
10Ω
50MΩ

## Slide 13
4. A student experimenting with a solar cell connects a 1000Ω voltmeter across it and observes a potential difference of 1.0 V. Using a different, extremely high resistance digital voltmeter, the reading is larger, 1.2 V. Why the difference? What is the internal resistance of the solar cell?
The first voltmeter had a small resistance, it allowed current to flow through it, hence increasing the internal resistance of the cell. The second voltmeter has an infinite resistance, it allows no current to flow, so it measures the actual Emf.
Emf = 1.2 V
lost volts = 0.2 V = Ir
Emf = IR + Ir
1.2 = Ix1000 + 0.2
I = 1/1000 = 0.001 A = 1 mA
r = Ir/I = 0.2/0.001 = 200 Ω
V
1000Ω
Infinite resistance
V

## Slide 14
5. A 9.0 V battery has an internal resistance of 12.0 .
(a) What is the potential difference across its terminals when it is supplying a current of 50.0 mA?
(b) What is the maximum current this battery could supply?
(c)Draw a sketch graph to show how the terminal potential difference varies with the current supplied if the internal resistance remains constant. How could the internal resistance be obtained from the graph?
Emf = V + lost volts = IR + Ir
V = Emf – Ir = 9 - (50X10-3 A x 12 Ω) = 8.4 V
Maximum current happens when R = 0
Emf = I (R + r) I = Emf/(R+r) = Emf/r = 9 V/12 Ω = 0.75A
(c)
I/A
V/V
Internal resistance = r = -gradient
Emf

## Slide 15
6. A cell in a hearing aid supplies a current of 25.0 mA through a resistance of 400 . When the wearer turns up the volume, the resistance is changed to 100  and the current rises to 60 mA. What is the emf and internal resistance of the cell?
R/Ω | I/mA | V/V
400 | 25 | 10
100 | 60 | 6
Plotting a graph of V vs I using the two points :
Gradient = (10-6)/(25-60)x10-3 = -114.3
r = -gradient = 114.3Ω
Emf = I (R + r) =
Emf = 25x10-3 (400 +114.3) = 12.86 V
Or Emf = 60x10-3 (100 +114.3) = 12.86 V
I/mA
V/V
10
25
60
6

## Slide 16
7. A battery is connected in series with a variable resistor and an ammeter. When the resistance of the resistor is 10  the current is 2.0 A. When the resistance is 5  the current is 3.8 A. Find the emf and the internal resistance of the battery.
R/Ω | I/A | V/V
10 | 2.0 | 20
5 | 3.8 | 19
Plotting a graph of V vs I using the two points :
Gradient = (20-19)/(2.0-3.8) = -0.55
r = -gradient = 0.55Ω
Emf = I (R + r) =
Emf = 2.0 (10+0.55) = 21.1 V
Or Emf = 3.8 (5+0.55) = 21.1 V
I/A
V/V
20
2.0
3.8
19

## Slide 17
9. When a cell is connected directly across a high resistance voltmeter the reading is 1.50 V. When the cell is shorted through a low resistance ammeter the current is 2.5 A. What is the emf and internal resistance of the cell?
Emf = 1.5 V
Imax = 2.5A
I = Emf/(R+r)
Imax happens when R=0
Imax = 1.5/r
r = Emf/Imax = 0.6 Ω